## Slide 1: ET 8403
INFORMATION THEORY AND CODING
Dr. Joseph.S.Salawa
0754556575

## Slide 2: Introduction
What is Information Theory?
IT is a branch of math (a strictly deductive system). (C. Shannon)
General statistical concept of communication. (N. Wiener, What is IT?)
It was build upon the work of Shannon (1948)
It answers to two fundamental questions in Communications Theory:
What is the fundamental limit for information compression?
What is the fundamental limit on information transmission rate over a communications channel?

## Slide 3: Digital Communications Systems
The fundamental problem of communication is that of reproducing at one point either exactly or approximately a message selected at another point. (Claude Shannon: A Mathematical Theory of Communications, 1948)

## Slide 4
Source
Source Coder: Convert an analog or digital source into bits.
Channel Coder: Protection against errors/erasures in the channel.
Modulator: Each binary sequence is assigned to a waveform
Channel: Physical Medium to send information from transmitter to receiver. Source of randomness.
Demodulator, Channel Decoder, Source Decoder, Sink.
Modulator + Channel = Discrete Channel.

## Slide 5: Model of a Digital Communication System
Destination
Decoding
Communication
Channel
Coding
Information
Source
Message
e.g. English symbols
Encoder
e.g. English to 0,1 sequence
Can have noise
or distortion
Decoder
e.g. 0,1 sequence to English

## Slide 6: Communication Channel Includes

## Slide 7: Shannon’s Definition of Communication
“The fundamental problem of communication is that of reproducing at one point either exactly or approximately a message selected at another point.”
“Frequently the messages have meaning”
“... [which is] irrelevant to the engineering problem.”

## Slide 8: Shannon Wants to…
Shannon wants to find a way for “reliably” transmitting data throughout the channel at “maximal” possible rate.
For example, maximizing the speed of ADSL @ your home
Destination
Decoding
Communication
Channel
Coding
Information
Source

## Slide 9: Shannon’s Vision
Data
Source
Encoding
Channel
Source Decoding
User
Channel Encoding
Channel Decoding

## Slide 10: Example: Disk Storage
Data
Zip
Channel
Unzip
User
Add CRC
Verify CRC

## Slide 11: In terms of Information Theory Terminology
Zip
Source
Encoding
=
Data Compression
Add CRC
Channel Encoding
=
Unzip
Source Decoding
=
Verify CRC
Channel Decoding
=
Data Decompression
Error Protection
Error Correction

## Slide 12: Example: VCD and DVD
Moive
MPEG
Encoder
CD/DVD
MPEG Decoder
TV
RS Encoding
RS Decoding
RS stands for Reed-Solomon Code.

## Slide 13: Example: Cellular Phone
Speech Encoding
Channel
Speech Decoding
CC Encoding
CC Decoding
CC stands for Convolutional Code.
GSM/CDMA

## Slide 14: Example: WLAN IEEE 802.11b
Data
Zip
Channel
Unzip
User
CC Encoding
CC Decoding
CC stands for Convolutional Code.
IEEE 802.11b

## Slide 15: Shannon Theory
The original 1948 Shannon Theory contains:
  Measurement of Information
  Source Coding Theory
  Channel Coding Theory

## Slide 16: Measurement of Information
Shannon’s first question is
“How to measure information
in terms of bits?”
= ? bits
= ? bits

## Slide 17: Or this…
= ? bits
= ? bits

## Slide 18: All events are probabilistic!
Using Probability Theory, Shannon showed that there is only one way to measure information in terms of number of bits:
called the entropy function

## Slide 19: For example
Tossing a dice:
  Outcomes are 1,2,3,4,5,6
  Each occurs at probability 1/6
  Information provided by tossing a dice is

## Slide 20: Wait! It is nonsense!
The number 2.585-bits is not an integer!!
What does you mean?

## Slide 21: Shannon’s First Source Coding Theorem
Shannon showed:
“To reliably store the information generated by some random source X, you need no more/less than, on the average, H(X) bits for each outcome.”

## Slide 22: Meaning:
If I toss a dice 1,000,000 times and record values from each trial
1,3,4,6,2,5,2,4,5,2,4,5,6,1,….
In principle, I need 3 bits for storing each outcome as 3 bits covers 1-8. So I need 3,000,000 bits for storing the information.
Using ASCII representation, computer needs 8 bits=1 byte for storing each outcome
The resulting file has size 8,000,000 bits

## Slide 23: But Shannon said:
You only need 2.585 bits for storing each outcome.
So, the file can be compressed to yield size
2.585x1,000,000=2,585,000 bits
Optimal Compression Ratio is:

## Slide 24: Let’s Do Some Test!
 | File Size | Compression Ratio
No Compression | 8,000,000 bits | 100%
Shannon | 2,585,000 bits | 32.31%
Winzip | 2,930,736 bits | 36.63%
WinRAR | 2,859,336 bits | 35.74%

## Slide 25: But With 50 Years of Hard Work
We have discovered a lot of good codes:
  Hamming codes
  Convolutional codes,
  Concatenated codes,
  Low density parity check (LDPC) codes
  Reed-Muller codes
  Reed-Solomon codes,
  BCH codes,
  Finite Geometry codes,
  Cyclic codes,
  Golay codes,
  Goppa codes
  Algebraic Geometry codes,
  Turbo codes
  Zig-Zag codes,
  Accumulate codes and Product-accumulate codes,
  …
We now come very close to the dream Shannon had 50 years ago! 

## Slide 26: Nowadays…
Source Coding Theorem has applied to
Channel Coding Theorem has applied to
Image
Compression
Data
Compression
Audio/Video
Compression
Audio
Compression
MPEG
MP3
VCD/DVD – Reed-Solomon Codes
Wireless Communication – Convolutional Codes
Optical Communication – Reed-Solomon Codes
Computer Network – LT codes, Raptor Codes
Space Communication

## Slide 27
Shannon's information theory deals with limits on data compression (source coding) and reliable data transmission (channel coding) { How much can data can be compressed?
{ How fast can data be reliably transmitted over a noisy channel?
Two basic \point-to-point" communication theorems (Shannon 1948)
{ Source coding theorem: the minimum rate at which data can be compressed losslessly is the entropy rate of the source
{ Channel coding theorem: The maximum rate at which data can be reliably transmitted is the channel capacity of the channel

## Slide 28: Axiomatic Approach

## Slide 30: Conditional Probability

## Slide 31: Bayes Rule

## Slide 32: Independence between Events

## Slide 34: What is Information?

## Slide 36
Entropy ??
NEXT LECTURE
Thank you