## Slide 1
FILTER CIRCUIT.
What is the Filter ?
A filter is a circuit that is designed to pass signals with desired frequencies and reject or attenuate other signals.
As a frequency-selective device, a filter can be used to limit the frequency spectrum of a signal to some specified band of frequencies.
Filters are the circuits used in radio and TV receivers to allow us to select one desired signal out of a multitude of broadcast signals in the environment.

## Slide 2
Any Filter Circuit can be classified as ;
(i ) Passive Filter (ii) Active Filter .
A filter is a passive filter if it consists of only passive elements R, L, and C. And,
It is said to be an active filter if it consists of active elements (such as transistors and Opamps in addition to passive elements R, L, and C.

## Slide 3
There are four types of filters whether passive or Active. Which are;
1. A lowpass filter passes low frequencies and stops high frequencies,
2. A highpass filter passes high frequencies and rejects low frequencies,
3. A bandpass filter passes frequencies within a frequency band and blocks or attenuates frequencies outside the band,
4. A bandstop filter passes frequencies outside a frequency band and blocks or attenuates frequencies within the band, as shown ideally

## Slide 4
Lowpass Filter.
A typical lowpass filter is formed when the output of an RC circuit is taken off the capacitor . The transfer function of the figure below is obtained as;