## Slide 1: Characteristics of Measurement Instruments
By
Candida Nakida Mwisomba

## Slide 2: Performance characteristics
Static characteristics
The set of criteria defined for the instrument, which are used to measure quantities which are slowly varying with time or mostly constant i.e. do not vary with time is called static characteristics.
Dynamic characteristics
When the quantity under measurement change rapidly with time, it is necessary to study the dynamic relations existing between input and output which is expressed as differential equation.
The set of criteria defined based on such dynamic differential equation is called dynamic characteristics.

## Slide 3
STATIC AND DYNAMIC CHARACTERISTICS

## Slide 4: Static characteristics
Accuracy
Precision
Error
Sensitivity
Resolution
Threshold
Linearity
Zero drift
Reproducibility
Stability

## Slide 5: Static characteristics…
1. Accuracy:
Degree of closeness which the instrument reading approaches the true value of the quantity to be measured.
It indicates the ability of an instrument to indicate true value of the quantity.

## Slide 6: Static characteristics…
2. Precision:
It is the measure of a consistency or repeatability of a measurement.
It denotes the closeness with which the individual measurements are departed or distributed about the average of numbers of measured values.
High precision may not have high accuracy.
Types of Precision
Conformity
Number of significant figures

## Slide 7: Static characteristics
Conformity
Error created due to limitation of scale reading is a precision error. e.g. resistor value is 2385702 Ω is read as 2.4MΩ
Significant figures
Precision is obtained from number of significant figures. e.g. 110Ω can be specified as 109Ω or 111Ω thus 3 significant figures. If it is specified as 110.0Ω then it may be 110.1Ω or 109.9Ω thus four significant figures.
Greater the significant figures greater is the precision

## Slide 8: Static characteristics
3. Error:
The algebraic difference between the indicated value and the true value of a quantity to be measured is called an error.
Error of 1 unit is negligible when measure in order of 1000 units
Error of 1 unit is significant when measure in order of 5 units.
where,
– error or absolute error
– measured value of a quantity
– true value of a quantity
Note: Instead of specifying absolute error, the relative or percentage of error is specified.

## Slide 9: Static characteristics
Relative error():
percentage relative error():
relative accuracy(A):

## Slide 10: Static characteristics
percentage accuracy():
error as a % of full scale reading
Where;
f.s.d – full scale deflection

## Slide 11: Static characteristics
4. Sensitivity:
The ratio of change in output of an instrument to a change in the value of quantity to be measured.

## Slide 12: Static characteristics

## Slide 13: Static characteristics
For manufactures
i.e.
Reciprocal of sensitivity is called inverse sensitivity or deflection factor
Unit: sensitivity - mm/μA, mm/Ω, counts/V etc.;
Deflection meter - μA/mm, Ω/mm, V/counts etc.;
Sensitivity should be high, to achieve this the range of instrument must not exceed the value to be measured.

## Slide 14: Static characteristics…
5. Resolution:
The smallest increment in the value of measurand that results in a detectable increment in the output.
It is expressed in the percentage of measurand range.
Resolution means smallest measurable input change.
6. Threshold
If the input is slowly varied from zero, the output does not change until some minimum value of the input is exceeded.
This minimum value of input is called threshold.
Threshold is the smallest measurable input.

## Slide 15: Static characteristics
7. Linearity:
The closeness to which a curve approximate a straight line
It is defined as a maximum deviation of the actual calibration curve(o/put) from the idealized straight line , expressed as a % of a full scale reading or % of actual reading.

## Slide 16: Static characteristics
8. Zero drift/Bias
The deviation of the instrument output with time from its zero value, when the variable to be measured is a constant. This can also be called the constant error which exist over the full range of measurement of an instrument.
9. Reproducibility
It is the degree of closeness with which a given value may be repeatedly measured.
Reproducibility and repeatability are a measure of the closeness with which a given input may be measured again and again.

## Slide 17: Static characteristics
10. Stability:
Ability of an instrument to retain its performance throughout its specified operating life and the storage life.
Tolerance:
The maximum allowable error in the measurement is specified in terms of some value which is called tolerance

## Slide 18: Dynamic characteristics
Speed of response
Fidelity
Lag
Dynamic error

## Slide 19: Dynamic characteristics
1. Speed of response
It gives information about how fast the system reacts to the changes in the input.
2. Fidelity
It is defined as the degree to which an instrument indicates the changes in the measured variable without dynamic error.
3. Lag
Delay in the response of a system.
Retardation lag: response of the system begins immediately after a change in a variable has occurred.
Time delay: response begins after sometime called dead time, after application of input.

## Slide 20: Dynamic characteristics
4. Dynamic error
The difference between the true value of a variable to be measured changing with time and a value indicate by the measurement system assuming zero static error.

## Slide 21: QUESTIONS
???

## Slide 22: Discussion
Significance of measurement with examples
Evolution of instruments
Electronic measurement
Elements of a measuring instrument
Static characteristics
Dynamic characteristics