## Slide 1
Signals and Systems
Feedback, Poles, and Fundamental Modes
April 2024
Presented by Nyatega, C.O

## Slide 2: Feedback, Poles, and Fundamental Modes
Verbal descriptions: preserve the rationale.
“To reduce the number of bits needed to store a sequence of large numbers that are nearly equal, record the ﬁrst number, and then record successive diﬀerences.”
Diﬀerence equations: mathematically compact.
y[n] = x[n] − x[n − 1]
−1
Delay
Block diagrams: illustrate signal ﬂow paths.
x[n] +
y[n]
Operator representations: analyze systems as polynomials.
Y = (1 − R) X

## Slide 3: Last Time: Feedback, Cyclic Signal Paths, and Modes
Systems with signals that depend on previous values of the same signal are said to have feedback.
Example: The accumulator system has feedback.
Delay
+
X Y
−1
Delay
+
X Y
By contrast, the diﬀerence machine does not have feedback.

## Slide 4: Last Time: Feedback, Cyclic Signal Paths, and Modes
The eﬀect of feedback can be visualized by tracing each cycle through the cyclic signal paths.
Delay
+
p0
X Y
x[n] = δ[n]
y[n]
n
n
−1 0 1 2 3 4
−1 0 1 2 3 4
Each cycle creates another sample in the output.

## Slide 5: Last Time: Feedback, Cyclic Signal Paths, and Modes
The eﬀect of feedback can be visualized by tracing each cycle through the cyclic signal paths.
Delay
+
p0
X Y
x[n] = δ[n]
y[n]
n
n
−1 0 1 2 3 4
−1 0 1 2 3 4
Each cycle creates another sample in the output.

## Slide 6: Last Time: Feedback, Cyclic Signal Paths, and Modes
The eﬀect of feedback can be visualized by tracing each cycle through the cyclic signal paths.
Delay
+
p0
X Y
x[n] = δ[n]
y[n]
n
n
−1 0 1 2 3 4
−1 0 1 2 3 4
Each cycle creates another sample in the output.

## Slide 7: Last Time: Feedback, Cyclic Signal Paths, and Modes
The eﬀect of feedback can be visualized by tracing each cycle through the cyclic signal paths.
Delay
+
p0
X Y
n
−1 0 1 2 3 4
x[n] = δ[n]
n
−1 0 1 2 3 4
y[n]
Each cycle creates another sample in the output.
The response will persist even though the input is transient.

## Slide 8: Geometric Growth: Poles
n
−1 0 1 2 3 4
p0 = 0.5
y[n]
These unit-sample responses can be characterized by a single number
— the pole — which is the base of the geometric sequence.
Delay
+
p0
X Y
y[n] =
n
p0 , if n >= 0; 0, otherwise.
n
−1 0 1 2 3 4
p0 = 1
y[n]
n
y[n]
−1 0 1 2 3 4
p0 = 1.2

## Slide 9: Check Yourself
How many of the following unit-sample responses can be represented by a single pole?
n
n
n
n
n

## Slide 10: Check Yourself
How many of the following unit-sample responses can be represented by a single pole? 3
n
n
n
n
n

## Slide 11: Geometric Growth
The value of p0 determines the rate of growth.
y[n]
y[n]
y[n]
y[n]
−1
0
1
z
p0 < −1:
magnitude diverges, alternating sign magnitude converges, alternating sign magnitude converges monotonically magnitude diverges monotonically
−1 < p0 < 0:
0 < p0 < 1:
p0 > 1:

## Slide 12: Second-Order Systems
The unit-sample responses of more complicated cyclic systems are more complicated.
+
X Y
R
1.6
R
−0.63
y[n]
n
−1 0 1 2 3 4 5 6 7 8
Not geometric. This response grows then decays.

## Slide 13: Factoring Second-Order Systems
Factor the operator expression to break the system into two simpler systems (divide and conquer).
R
1.6
R
−0.63
+
X Y
Y = X + 1.6RY − 0.63R
2Y
2
(1 − 1.6R + 0.63R ) Y = X
(1 − 0.7R)(1 − 0.9R) Y = X

## Slide 14: Factoring Second-Order Systems
The factored form corresponds to a cascade of simpler systems.
(1 − 0.7R)(1 − 0.9R) Y = X
+
+
X
Y
Y2
0.7 R
(1 − 0.7R) Y2 = X
0.9 R
(1 − 0.9R) Y = Y2
+
+
X
Y
Y1
0.9 R
(1 − 0.9R) Y1 = X
0.7 R
(1 − 0.7R) Y = Y1
The order doesn’t matter (if systems are initially at rest).

## Slide 15: Factoring Second-Order Systems
The unit-sample response of the cascaded system can be found by multiplying the polynomial representations of the subsystems.
Y = 1 = 1 × 1
X (1 − 0.7R)(1 − 0.9R) (1 − 0.7R) (1 − 0.9R)
_ _
_
_
= (1 + 0.
7R + 0.
2 2
7 R + 0.
3 3
7 R + · · ·
2 2
) × (1 + 0.9R + 0.9 R + 0.93 3 + · · · )
R
Multiply, then collect terms of equal order:
Y X
= 1 + (0.7 + 0.9)R + (0.72 + 0.7 × 0.9 + 0.92)R
2
+ (0.73 + 0.72 × 0.9 + 0.7 × 0.92 + 0.93)R
3 + · · ·

## Slide 16: Multiplying Polynomial
Graphical representation of polynomial multiplication.
Y
Collect terms of equal order:
Y
X
= (1 + aR + a2R
3 2
R + · · ·) × (1 + bR + b R
2 + a3 2 + b3
3
R + · · ·)
1
a
a2
R
R2
a3
R3
+
1
b
b2
R
R2
b3
R3
+
... ...
...
...
X
Y
= 1 + (a + b)R + (a2 + ab + b2)
2 3 2 2 3 3
R + (a + a b + ab + b )R + · · ·
X

## Slide 17: Multiplying Polynomials
n
−1 0 1 2 3 4 5 6 7 8
y[n]
Tabular representation of polynomial multiplication.
2 3 3 2 2 3 3
(1 + aR + a2R + a R + · · ·) × (1 + bR + b R + b R + · · ·)
b2R2 b3R3
1 bR · · ·
1
1 bR
b2R2
b3R3
aR
aR abR2
ab2R3
a2R2
a2R2
a2bR3
a2b2R4
a2b3R5
a3R3
a3R3
a3bR4
a3b2R5
a3b3R6
· · · · · · · · · · · · · · ·
ab3R4 · · ·
· · ·
· · ·
· · ·
· · ·
Group same powers of R by following reverse diagonals:
Y X
2 3 2 2 3 3
= 1 + (a + b)R + (a2 + ab + b2)R + (a + a b + ab + b )R + · · ·

## Slide 18: Partial Fractions
Use partial fractions to rewrite as a sum of simpler parts.
R
1.6
R
−0.63
+
X Y
Y 1
=
2 = 1 = 4.5 − 3.5
X 1 − 1.6R + 0.63R (1 − 0.9R)(1 − 0.7R) 1 − 0.9R 1 − 0.7R

## Slide 19: Second-Order Systems: Equivalent Forms
+
0.9
R
4.5
+
−3.5
R
0.7
+
X
Y
The sum of simpler parts suggests a parallel implementation.
Y = 4.5 − 3.5
X 1 − 0.9R 1 − 0.7R
Y1
Y2
If x[n] = δ[n] then y1[n] = 0.9n and y2[n] = 0.7n for n ≥ 0.
Thus, y[n] = 4.5(0.9)n − 3.5(0.7)n for n ≥ 0.

## Slide 20: Partial Fractions
Graphical representation of the sum of geometric sequences.
y1[n] = 0.9n for n ≥ 0
n
−1 0 1 2 3 4 5 6 7 8
y2[n] = 0.7n for n ≥ 0
n
−1 0 1 2 3 4 5 6 7 8
y[n] = 4.5(0.9)n − 3.5(0.7)n
for n ≥ 0
n
−1 0 1 2 3 4 5 6 7 8

## Slide 21: Partial Fractions
Partial fractions provides a remarkable equivalence.
+
X Y
+
0.9
R
4.5
+
−3.5
R
0.7
+
R
1.6
R
−0.63
Y1
X
Y
Y2
→ follows from thinking about system as polynomial (factoring).

## Slide 22: Poles
The key to simplifying a higher-order system is identifying its poles.
Poles are the roots of the denominator of the system functional
1
when R → .
z
Start with system functional:
Y 1 1 1
= 2 = =
X 1 − 1.6R+0.63R (1−p0R)(1−p1R) (1−0.7R) (1−0.9R)
-. p0..=,.0.7 .. -. p1..=,.0.9 ..
1
z
Substitute R →
and ﬁnd roots of denominator:
2 2
Y X
z
z
=
=
2
z −1.
6z +0
= (
.63 z−0.7) (z−0.9)
1 −
1
1.6 + 0.63
z
z2
The poles are at 0.7 and 0.9.
-.z0..=,.0.7.. -.z1..=,.0.9..

## Slide 23: Check Yourself
Consider the system described by
1 1 1
y[n] = − 4 y[n − 1] + 8 y[n − 2] + x[n − 1] − 2 x[n − 2]
How many of the following are true?
2 4
2
The unit sample response converges to zero.
There are poles at z = 1 and z = 1 .
There is a pole at z = 1 .
There are two poles.
None of the above

## Slide 26: Check Yourself
Consider the system described by
2 4
2
1 1 1
y[n] = − 4 y[n − 1] + 8 y[n − 2] + x[n − 1] − 2 x[n − 2]
How many of the following are true? 2
The unit sample response converges to zero.
There are poles at z = 1 and z = 1 .
There is a pole at z = 1 .
There are two poles.
None of the above

## Slide 27
Population Growth

## Slide 28
Population Growth

## Slide 29
Population Growth

## Slide 30
Population Growth

## Slide 31
Population Growth

## Slide 32: Check Yourself
What are the pole(s) of the Fibonacci system?
1. 1
1 and −1
−1 and −2
1.618 . . . and −0.618 . . .
none of the above

## Slide 33: Check Yourself
What are the pole(s) of the Fibonacci system?
Diﬀerence equation for Fibonacci system:
y[n] = x[n] + y[n − 1] + y[n − 2]
System functional:
Y 1
H = =
X 1 − R − R2
Denominator is second order → 2 poles.

## Slide 34: Check Yourself
Find the poles by substituting R → 1/z in system functional.
Y 1
z2
H = =
X 1 − R − R
2
→
1 − −
1
1 1
=
z2 − z − 1
z z2
Poles are a√t
z = 1 ±2 5 =
φ or − 1
φ
where φ represents the “golden ratio”
1 + √5
2
φ =
≈ 1.618
The two poles are at
z0 = φ ≈ 1.618 and
1
0.618
z1 = −φ ≈ −

## Slide 35: Check Yourself
What are the pole(s) of the Fibonacci system? 4
1. 1
1 and −1
−1 and −2
1.618 . . . and −0.618 . . .
none of the above

## Slide 36: Example: Fibonacci’s Bunnies
Each pole corresponds to a fundamental mode.
1
φ ≈ 1.618 and − φ ≈ −0.618
One mode diverges, one mode oscillates!
n
−1 0 1 2 3 4
φn
n
−1 0 1 2 3 4
1
−φ
3 4
n

## Slide 37: Example: Fibonacci’s Bunnies
The unit-sample response of the Fibonacci system can be written as a weighted sum of fundamental modes.
φ 1
Y 1
√5
φ√5 1
H = =
=
+
2
X 1 − R − R 1 − φR
1 + R
φ
φ 1
n −n
h[n] = √5 φ + φ√5 (−φ) ; n ≥ 0
But we already know that h[n] is the Fibonacci sequence f :
f : 1, 1, 2, 3, 5, 8, 13, 21, 34, 55, 89, . . .
Therefore we can calculate f [n] without knowing f [n − 1] or f [n − 2] !

## Slide 38: Complex Poles
What if a pole has a non-zero imaginary part?
Example:
Y 1
=
2
X 1 − R1 + R
z
2
=
=
z
1 − +
1 1
z
2
2
z − z + 1
√
1 3
±jπ/3
2 2
Poles are z = ± j = e
.
What are the implications of complex poles?

## Slide 39: Complex Poles
�
�
Partial fractions work even when the poles are complex.
Y = 1 × 1 = 1
X 1 − e jπ/3R 1 − e−jπ/3R j√3
e jπ/3 e−jπ/3
1 − e jπ/3R − 1 − e−jπ/3R
There are two fundamental modes (both geometric sequences):
e jnπ/3 = cos(nπ/3) + j sin(nπ/3) and e−jnπ/3 = cos(nπ/3) − j sin(nπ/3)
n
n

## Slide 40: Complex Poles
Complex modes are easier to visualize in the complex plane.
e jnπ/3 = cos(nπ/3) + j sin(nπ/3)
Re
Im
e j0π/3
e j2π/3 e j1π/3
e j3π/3
e j4π/3
e j5π/3
Re
Im
e j0π/3
e j5π/3
e j4π/3
e j3π/3
e j2π/3
e j1π/3
n
e−jnπ/3 = cos(nπ/3) − j sin(nπ/3)
n

## Slide 41: Complex Poles
The output of a “real” system has real values.
y[n] = x[n] + y[n − 1] − y[n − 2]
Y 1
H = =
X 1 − R + R2
= 1 × 1
1 − e jπ/3R 1 − e−jπ/3R
= 1
j√3
e jπ/3 e−jπ/3
1 − e jπ/3R − 1 − e−jπ/3R
1
h[n] = √ e
j 3
j(n+1)π/
− e
3 −j(n+1)π/3
= √3 sin
2 (n + 1)π 3
h[n] 1
−1
n
(

## Slide 42: Check Yourself
Unit-sample response of a system with poles at z = re±jΩ.
n
Which of the following is/are true?
r < 0.5 and Ω ≈ 0.5
0.5 < r < 1 and Ω ≈ 0.5
r < 0.5 and Ω ≈ 0.08
0.5 < r < 1 and Ω ≈ 0.08
none of the above

## Slide 43: Check Yourself
Unit-sample response of a system with poles at z = re±jΩ.
n
Which of the following is/are true? 2
r < 0.5 and Ω ≈ 0.5
0.5 < r < 1 and Ω ≈ 0.5
r < 0.5 and Ω ≈ 0.08
0.5 < r < 1 and Ω ≈ 0.08
none of the above

## Slide 44: Check Yourself
R
R
R
+
X
Y
How many of the following statements are true?
This system has 3 fundamental modes.
All of the fundamental modes can be written as geometrics.
Unit-sample response is y[n] : 0, 0, 0, 1, 0, 0, 1, 0, 0, 1, 0, 0, 1 . . .
Unit-sample response is y[n] : 1, 0, 0, 1, 0, 0, 1, 0, 0, 1, 0, 0, 1 . . .
One of the fundamental modes of this system is the unit step.

## Slide 45: Check Yourself
R
R
R
+
X
Y
How many of the following statements are true? 4
This system has 3 fundamental modes.
All of the fundamental modes can be written as geometrics.
Unit-sample response is y[n] : 0, 0, 0, 1, 0, 0, 1, 0, 0, 1, 0, 0, 1 . . .
Unit-sample response is y[n] : 1, 0, 0, 1, 0, 0, 1, 0, 0, 1, 0, 0, 1 . . .
One of the fundamental modes of this system is the unit step.

## Slide 46: Summary
Systems composed of adders, gains, and delays can be characterized by their poles.
The poles of a system determine its fundamental modes.
The unit-sample response of a system can be expressed as a weighted sum of fundamental modes.
These properties follow from a polynomial interpretation of the sys­ tem functional.