## Slide 1: Assembly Language Programming of 8085

## Slide 2: Topics
Introduction
Programming model of 8085
Instruction set of 8085
Example Programs
Addressing modes of 8085
Instruction & Data Formats of 8085

## Slide 3: 1. Introduction
A microprocessor executes instructions given by the user
Instructions should be in a language known to the microprocessor
Microprocessor understands the language of 0’s and 1’s only
This language is called Machine Language

## Slide 4
For e.g.
01001111
  Is a valid machine language instruction of 8085
  It copies the contents of one of the internal registers of 8085 to another

## Slide 5: A Machine language program to add two numbers
00111110
00000010
00000110
00000100
10000000
;Copy value 2H in register A
;Copy value 4H in register B
;A = A + B

## Slide 6: Assembly Language of 8085
It uses English like words to convey the action/meaning called as MNEMONICS
For e.g.
MOV
ADD
SUB
to indicate data transfer to add two values
to subtract two values

## Slide 7: Assembly language program to add two numbers
MVI A, 2H ;Copy value 2H in register A MVI B, 4H ;Copy value 4H in register B ADD B ;A = A + B
Note:
Assembly language is specific to a given processor
For e.g. assembly language of 8085 is different than that of Motorola 6800 microprocessor

## Slide 8: Microprocessor understands Machine Language only!
Microprocessor cannot understand a program written in Assembly language
A program known as Assembler is used to convert a Assembly language program to machine language
Assembly Language Program
Assembler Program
Machine Language Code

## Slide 9: Low-level/High-level languages
Machine language and Assembly language are both
  Microprocessor specific (Machine dependent)
so they are called
  Low-level languages
Machine independent languages are called
  High-level languages
  For e.g. BASIC, PASCAL,C++,C,JAVA, etc.
  A software called Compiler is required to convert a high-level language program to machine code

## Slide 10: 2. Programming model of 8085
Accumulator
ALU
Flags
Instruction Decoder
Register Array
Memory Pointer Registers
Timing and Control Unit
16-bit Address Bus
8-bit Data Bus
Control Bus

## Slide 11: Accumulator (8-bit)
B (8-bit)
D (8-bit)
E (8-bit)
H (8-bit)
L (8-bit)
Stack Pointer (SP) (16-bit) Program Counter (PC) (16-bit)
Flag Register (8-bit)
S Z AC P
C (8-bit)
CY
16- Lines Unidirectional
8- Lines Bidirectional

## Slide 12: Overview: 8085 Programming model
Six general-purpose Registers
Accumulator Register
Flag Register
Program Counter Register
Stack Pointer Register

## Slide 13
1. Six general-purpose registers
–
–
B, C, D, E, H, L
Can be combined as register pairs to perform 16-bit operations (BC, DE, HL)
2. Accumulator – identified by name A
–
–
–
–
This register is a part of ALU 8-bit data storage
Performs arithmetic and logical operations
Result of an operation is stored in accumulator

## Slide 14: 3. Flag Register
–
–
This is also a part of ALU 8085 has five flags named
•
•
•
•
•
Zero flag (Z) Carry flag (CY) Sign flag (S) Parity flag (P)
Auxiliary Carry flag (AC)

## Slide 15
These flags are five flip-flops in flag register
Execution of an arithmetic/logic operation can
set or reset these flags
Condition of flags (set or reset) can be tested through software instructions
8085 uses these flags in decision-making process

## Slide 16
Program Counter (PC)
  A 16-bit memory pointer register
  Used to sequence execution of program instructions
  Stores address of a memory location
    where next instruction byte is to be fetched by the 8085
  when 8085 gets busy to fetch current instruction from memory
    PC is incremented by one
    PC is now pointing to the address of next instruction

## Slide 17: 5. Stack Pointer Register
–
–
–
a 16-bit memory pointer register Points to a location in Stack memory
Beginning of the stack is defined by loading a 16-bit address in stack pointer register

## Slide 18: 3.Instruction Set of 8085
•
Consists of
–
–
74 operation codes, e.g. MOV 246 Instructions, e.g. MOV A,B
•
8085 instructions can be classified as
Data Transfer (Copy)
Arithmetic
Logical and Bit manipulation
Branch
Machine Control

## Slide 19: 1. Data Transfer (Copy) Operations
Load a 8-bit number in a Register
Copy from Register to Register
Copy between Register and Memory
Copy between Input/Output Port and Accumulator
Load a 16-bit number in a Register pair
Copy between Register pair and Stack memory

## Slide 20: Example Data Transfer (Copy) Operations Instructions
/
Load a 8-bit number 4F in register B
Copy from Register B to Register A
Load a 16-bit number 2050 in Register pair HL
Copy from Register B to Memory Address 2050
Copy between Input/Output Port and Accumulator
MVI B, 4FH
MOV A,B
LXI H, 2050H
MOV M,B
OUT 01H IN 07H

## Slide 21: 2. Arithmetic Operations
Addition of two 8-bit numbers
Subtraction of two 8-bit numbers
Increment/ Decrement a 8-bit number

## Slide 22: Example Arithmetic Operations / Instructions
Add a 8-bit number 32H to Accumulator
Add contents of Register B to Accumulator
Subtract a 8-bit number 32H from Accumulator
Subtract contents of Register C from Accumulator
Increment the contents of Register D by 1
Decrement the contents of Register E by 1
ADI 32H
ADD B
SUI 32H
SUB C
INR D
DCR E

## Slide 23: 3. Logical & Bit Manipulation Operations
AND two 8-bit numbers
OR two 8-bit numbers
Exclusive-OR two 8-bit numbers
Compare two 8-bit numbers
Complement
Rotate Left/Right Accumulator bits

## Slide 24: Example Logical & Bit Manipulation Operations / Instructions
Logically AND Register H with Accumulator
Logically OR Register L with Accumulator
Logically XOR Register B with Accumulator
Compare contents of Register C with Accumulator
Complement Accumulator
Rotate Accumulator Left
ANA H
ORA L
XRA B
CMP C
CMA RAL

## Slide 25: 4. Branching Operations
These operations are used to control the flow of program execution
1.Jumps
•
•
Conditional jumps Unconditional jumps
2.Call & Return
•
•
Conditional Call & Return Unconditional Call & Return

## Slide 26: Example Branching
Operations / Instructions
1. Jump to a 16-bit Address
2080H if Carry flag is SET
Unconditional Jump
Call a subroutine with its 16-bit Address
Return back from the Call
Call a subroutine with its 16-bit Address if Carry flag is RESET
Return if Zero flag is SET
JC 2080H
JMP 2050H CALL 3050H
RET
CNC 3050H
RZ

## Slide 27: 5. Machine Control Instructions
These instructions affect the operation of the processor. For e.g.
HLT NOP
Stop program execution
Do not perform any operation

## Slide 28: 4. Writing a Assembly Language Program
Steps to write a program
  Analyze the problem
  Develop program Logic
  Write an Algorithm
  Make a Flowchart
  Write program Instructions using Assembly language of 8085

## Slide 29: Program 8085 in Assembly language to add two 8- bit numbers and store 8-bit result in register C.
Analyze the problem
– Addition of two 8-bit numbers to be done
Program Logic
–
–
–
Add two numbers
Store result in register C Example
10011001 | (99H) A
+00111001 | (39H) D
11010010 | (D2H) C

## Slide 30: Translation to 8085 operations
1. Get two numbers
Add them
Store result
Stop
Load 1st no. in register D
Load 2nd no. in register E
Copy register D to A
Add register E to A
Copy A to register C
Stop processing
3. Algorithm

## Slide 31: 4. Make a Flowchart
Start
Load Registers D, E
Copy D to A
Add A and E
Copy A to C
Stop
Load 1st no. in register D
Load 2nd no. in register E
Copy register D to A
Add register E to A
Copy A to register C
Stop processing

## Slide 32: 5. Assembly Language Program
1. Get two numbers
Load 1st no. in register D
Load 2nd no. in register E
2. Add them
Copy register D to A
Add register E to A
3. Store result
a) Copy A to register C
4. Stop
a) Stop processing
MVI D, 2H MVI E, 3H
MOV A, D ADD E
MOV C, A
HLT

## Slide 33: Program 8085 in Assembly language to add two 8- bit numbers. Result can be more than 8-bits.
1. Analyze the problem
–
– Result of addition of two 8-bit numbers can be 9-bit
Example
10011001
+10011001
(99H) A
(99H) B
100110010 (132H)
The 9th bit in the result is called CARRY bit.
–

## Slide 34
How 8085 does it?
  Adds register A and B
  Stores 8-bit result in A
  SETS carry flag (CY) to indicate carry bit
10011001
10011001
A
+
B
99H
99H
1000111000101
A
CY
99H
10 32H

## Slide 35: Storing result in Register memory
•
10011001
A
32H
1
CY
Register C
Register B
Step-1 Copy A to C Step-2
Clear register B
Increment B by 1

## Slide 36: 2. Program Logic
Add two numbers
Copy 8-bit result in A to C
If CARRY is generated
– Handle it
Result is in register pair BC

## Slide 37: Translation to 8085 operations
Load two numbers in registers D, E
Add them
Store 8 bit result in C
Check CARRY flag
If CARRY flag is SET
  Store CARRY in register B
Stop
3. Algorithm
•
•
•
•
Load registers D, E
Copy register D to A Add register E to A
Copy A to register C
Use Conditional Jump instructions
Clear register B Increment B
Stop processing

## Slide 38: 4. Make a Flowchart
Start
Load Registers D, E
Copy D to A
Add A and E
Copy A to C
Stop
If CARRY NOT SET
Clear B
Increment B
False
True

## Slide 39: 5. Assembly Language Program
MVI D, 2H MVI E, 3H MOV A, D ADD E MOV C, A JNC END
MVI B, 0H INR B
END: HLT
Load registers D, E
•
•
Copy register D to A Add register E to A
Stop processing
•
•
Clear register B Increment B
Copy A to register C
Use Conditional Jump instructions

## Slide 40: 4. Addressing Modes of 8085
Format of a typical Assembly language instruction is given below-
[Label:] Mnemonic [Operands] [;comments]
HLT
MVI A, 20H
MOV M, A
;Copy A to memory location whose address is stored in register pair HL
LOAD: LDA 2050H ;Load A with contents of memory
location with address 2050H
READ: IN 07H
;Read data from Input port with address 07H

## Slide 41: The various formats of specifying operands are called addressing modes
•
•
Addressing modes of 8085
Register Addressing
Immediate Addressing
Memory Addressing
Input/Output Addressing

## Slide 42: 1. Register Addressing
Operands are one of the internal registers of 8085
Examples-
MOV A, B ADD C

## Slide 43: 2. Immediate Addressing
Value of the operand is given in the instruction itself
Example-
MVI A, 20H LXI H, 2050H ADI 30H
SUI 10H

## Slide 44: 3. Memory Addressing
One of the operands is a memory location
Depending on how address of memory location is specified, memory addressing is of two types
  Direct addressing
  Indirect addressing

## Slide 45: 3(a) Direct Addressing
16-bit Address of the memory location is specified in the instruction directly
Examples-
LDA 2050H ;load A with contents of memory
location with address 2050H
STA 3050H ;store A with contents of memory
location with address 3050H

## Slide 46: 3(b) Indirect Addressing
A memory pointer register is used to store the address of the memory location
Example-
MOV M, A ;copy register A to memory location whose address is stored in register pair HL
H L
30H
A
20H
50H
30H
2050H

## Slide 47: 4. Input/Output Addressing
8-bit address of the port is directly specified in the instruction
Examples-
IN 07H OUT 21H

## Slide 48: 5. Instruction & Data Formats
8085 Instruction set can be classified according to size (in bytes) as
1-byte Instructions
2-byte Instructions
3-byte Instructions

## Slide 49: 1. One-byte Instructions
Includes Opcode and Operand in the same byte
Examples-
Opcode | Operand | Binary Code | Hex Code
MOV | C, A | 0100 1111 | 4FH
ADD | B | 1000 0000 | 80H
HLT |  | 0111 0110 | 76H

## Slide 50: 1. Two-byte Instructions
First byte specifies Operation Code
Second byte specifies Operand
Examples-
Opcode | Operand | Binary Code | Hex Code
MVI | A, 32H | 0011 1110 | 3EH
 |  | 0011 0010 | 32H
MVI | B, F2H | 0000 0110 | 06H
 |  | 1111 0010 | F2H

## Slide 51: 1. Three-byte Instructions
First byte specifies Operation Code
Second & Third byte specifies Operand
Examples-
Opcode | Operand | Binary Code | Hex Code
LXI | H, 2050H | 0010 0001 | 21H
 |  | 0101 0000 | 50H
 |  | 0010 0000 | 20H
LDA | 3070H | 0011 1010 | 3AH
 |  | 0111 0000 | 70H
 |  | 0011 0000 | 30H

## Slide 52: Separate the digits of a hexadecimal numbers and store it in two different locations
LDA 2200H ANI F0H | ; Get the packed BCD ; Mask lower nibble | number
 | 0100 0101 | 45
 | 1111 0000 | F0
RRC | 0100 0000 | 40
RRC |  | 
•
•
RRC RRC
; Adjust higher digit as a lower digit.
0000 0100 after 4 rotations

## Slide 53: Contd.
STA 2300H
LDA 2200H
; Store the partial result
; Get the original BCD no.
ANI 0FH ; Mask higher nibble
0100 0100
0000 1111
45
0F
0000 0100 05
; Store the result
; Terminate program execution
STA 2301H
HLT

## Slide 54: Block data transfer
•
MVI C, 0AH
; Initialize counter i.e no. of bytes Store the count in Register C, ie ten
; Initialize source memory pointer Data Starts from 2200 location
; Initialize destination memory pointer
•
LXI H, 2200H
•
LXI D, 2300H
BK: MOV A, M
; Get byte from source memory block
i.e 2200 to accumulator.
; Store byte in the destination memory block i.e 2300 as stored in D-E pair
•
STAX D
•

## Slide 55: Contd.
INX H pointer
INX D pointer
; Increment source memory
; Increment destination memory
DCR C ; Decrement counter to keep track of bytes moved
JNZ BK ; If counter 0 repeat steps
HLT ; Terminate program