## Slide 1: DIGITAL ELECTRONICS
Friday, January 5, 2024
Mr. Cuthbert J. Karawa
Lecture 07
Functions of Combinational Logic
College of Information and Communication Technology (CoICT) Department Of Electronics And Telecommunications Engineering.
ET 8301

## Slide 2: Introduction
The tradition way of combinational circuit design involves simplification and realization of circuit using logic gates.
This method is effective for small circuit.
When the circuit is more complex, more number of gates are required with more number of wires between them.
Designing such circuits is time consuming and less reliable.

## Slide 3: Introduction
To avoid these problems several combination circuits available in integrated circuits are employed in the designing of digital systems.
Number of gates per package | Classification | Abbreviation
<10 | Small Scale Integration | SSI
10-99 | Medium Scale Integration | MSI
1000 | Large Scale Integration | LSI
10K | Very Large Scale Integration | VLSI

## Slide 4: Introduction
Most combinational circuits which available in IC are classified as MSI components
MSI components which available in IC includes adders, subtractors, multiplexers, demultiplexers, decoders, encoders and comparators.
These MSI are used to implement combinational circuits.

## Slide 5: Binary adder
Adder are important in computer and also in other types of digital system in which numerical data are processed.
The basic operations are the arithmetic operations which includes additions of binary digits.

## Slide 6: Binary adder
Half adder
Basic rules of binary addition are performed by a half adder, which has two binary inputs (A and B) and two binary outputs (Carry out and Sum).
The inputs and outputs can be summarized on a truth table.

## Slide 7: Binary adder
Half Adder
From truth table we get
The logic symbol and equivalent circuit are:

## Slide 8: Binary adder
Full Adder
  The full adder accepts two inputs bits and input carry and generates a sum output and an output carry.
  The truth table summarizes the operation.

## Slide 9: Binary adder
From the truth table we get
The logic symbol and equivalent circuit are:

## Slide 10: Exercise
Implement full adder by using two half adders.

## Slide 11: Binary adder
Parallel Adder
More often there a need to add two n bits numbers.
When adding two n bit number the two LSB are added to produce their sum and carry out bit.
Then the next two bits are added together with a carry generated from the addition of the first two bits to produce the sum and carry out bits
The process is repeated until the most significant bits are reached.

## Slide 12: Binary adder
Parallel Adder
To add two binary numbers a full adder is required for each bit in the numbers.
Therefore for 2-bit numbers two adders are needed for 3-bit numbers three adders are needed and so on
The carry output of each adder is connected to the carry input of the next higher order adder.
Two or more full-adders are connected to form parallel binary adders.

## Slide 13: Binary adder
Parallel Adder
Figure below shows a basic 2-bit parallel adder which is implemented with two full adder stages.

## Slide 14: Binary adder
Parallel Adders
A 4-bit adder is shown figure below.
The output carry (C4) is not ready until it propagates through all of the full adders. This is called ripple carry, delaying the addition process.

## Slide 15: Exercise
Determine the sum generated by the 3-bit parallel adder and show the intermediate carries when the binary number 101 and 011 are being added

## Slide 16: Comparators
The basic function of a comparator is to compare the magnitudes of two binary quantities to determine the relationship of those quantities.
The exclusive-NOR gate can be used as a basic comparator because its output is a 0 if the two input bits are not equal and a 1 if the input bits are equal.
Figure above shows the exclusive-NOR gate as a 2-bit comparator.

## Slide 17: Decoders
A decoder is a digital circuit that detects the presence of a specified combination of bits (code) on its inputs and indicates the presence of that code by a specified output level.
In general a decoder has multiple inputs and multiple outputs.
The are several types of decoder but the most common is n to 2n type of decoder e.g. 2 to 4,3 to 8 and 4 to 16 line decoders.

## Slide 18: Decoders
Example:
Show truth table and block diagram of 2 to 4 line decoder
Truth table
Block diagram
Inputs |  | Outputs |  |  | 
0 | 0 | 1 | 0 | 0 | 0
0 | 1 | 0 | 1 | 0 | 0
1 | 0 | 0 | 0 | 1 | 0
1 | 1 | 0 | 0 | 0 | 1

## Slide 19: Decoders
From truth table it can be observed that the output variables are mutually exclusive because only one output can be equal to 1 at any one time.
The output line whose value is equal to 1 represents the minterm equivalent of the binary number presently available in the input lines.

## Slide 20: Decoders
From truth table we can write
Figure: Implementation of 2 to 4 line decoder

## Slide 21: Decoders
.

## Slide 22: Decoders

## Slide 23: Decoders
.

## Slide 24: Decoders
Logic design using decoder
The number of inputs to each or gate can be minimized by implement the f’ instead of f and finally invert the OR output to get f.
Example:
  Implement the following functions using a decoder minimizing the number of inputs to be summed.

## Slide 25: Decoders
Logic design using decoder
The decoder in IC packages usually have an active low output. The truth table and symbol of such 2 to 4 line decoder.
These generate maxterms at their output and are useful in implementing canonical POS expression.
Inputs |  | Outputs |  |  | 
0 | 0 | 0 | 1 | 1 | 1
0 | 1 | 1 | 0 | 1 | 1
1 | 0 | 1 | 1 | 0 | 1
1 | 1 | 1 | 1 | 1 | 0

## Slide 26: Decoders

## Slide 27: Decoders
Logic design using decoder
Functions expressed in maxterm canonical forms can also be implemented using decoder.
Example: implement the following functions expressed in maxterm canonical form in two possible ways using a 3 to 8 decoder.

## Slide 28: Decoders
Decoders with Enable Input
On previous decoder one of the input is either 1 or 0 for active high and low outputs respectively.
Enable input is used for some application where more than one output need to be at 0 or 1 state.
Enable inputs are also useful in cascading decoders to increase their input and outputs lines.

## Slide 29: Decoders
Decoders with Enable Input
  The truth table and symbol of 2 to 4 line decoder with enable for uncomplemented (active high) output is as shown
Inputs |  |  | Outputs |  |  | 
E |  |  |  |  |  | 
0 | x | x | 0 | 0 | 0 | 0
1 | 0 | 0 | 1 | 0 | 0 | 0
1 | 0 | 1 | 0 | 1 | 0 | 0
1 | 1 | 0 | 0 | 0 | 1 | 0
1 | 1 | 1 | 0 | 0 | 0 | 1

## Slide 30: Decoders
Decoders with Enable Input
The enable input can also be included in decoder with complemented (active low) output as shown
Inputs |  |  | Outputs |  |  | 
E |  |  |  |  |  | 
0 | 0 | 0 | 0 | 1 | 1 | 1
0 | 0 | 1 | 1 | 0 | 1 | 1
0 | 1 | 0 | 1 | 1 | 0 | 1
0 | 1 | 1 | 1 | 1 | 1 | 0
1 | x | x | 1 | 1 | 1 | 1

## Slide 31: Encoders
An encoder has 2n inputs and n outputs.
Outputs the binary value of the selected (or active) input.
Performs the inverse operation of a decoder.
Some examples of encoders are 4to 2 line and 8 to 3 line encoders
Notes: ]\

## Slide 32: Encoders
Truth Table of 4-2line encoder
Block diagram of 4-2line encoder
X0 | X1 | X2 | X3 | Y1 | Y0
1 | 0 | 0 | 0 | 0 | 0
0 | 1 | 0 | 0 | 0 | 1
0 | 0 | 1 | 0 | 1 | 0
0 | 0 | 0 | 1 | 1 | 1
Notes: ]\

## Slide 33: Priority Encoders
If more than one input is active the higher order input has priority over the lower order input
The higher value is encoded at the output
A valid indicator is included to indicate whether or not the output is valid
Output is invalid (0) when no inputs are active.
Output is valid (1) when at least one input is active

## Slide 34: Priority Encoders
The truth table of 4-2 line priority encoder
X0 | X1 | X2 | X3 | Y1 | Y0 | Valid
0 | 0 | 0 | 0 | 0 | 0 | 0
1 | 0 | 0 | 0 | 0 | 0 | 1
x | 1 | 0 | 0 | 0 | 1 | 1
x | x | 1 | 0 | 1 | 0 | 1
x | x | x | 1 | 1 | 1 | 1

## Slide 35: Multiplexer
A multiplexer (MUX) selects one data line from two or more input lines and routes data from the selected line to the output
Multiplexer has a set of n address lines(select inputs) to select one of these inputs.
Multiplexer also has one or more enable inputs.

## Slide 36: Multiplexer
Symbol of 4-1 MUX

## Slide 37: Multiplexer
Truth table of 4 to 1 MUX
Row no. | E | Sel Line |  | Inputs |  |  |  | Output
0 | 0 | X | X | X | X | X | X | 0
1 | 1 | 0 | 0 | 0 | X | X | X | 0
2 | 1 | 0 | 0 | 1 | X | X | X | 1
3 | 1 | 0 | 1 | X | 0 | X | X | 0
4 | 1 | 0 | 1 | X | 1 | X | X | 1
5 | 1 | 1 | 0 | X | X | 0 | X | 0
6 | 1 | 1 | 0 | X | X | 1 | X | 1
7 | 1 | 1 | 1 | X | X | X | 0 | 0
8 | 1 | 1 | 1 | X | X | X | 1 | 1

## Slide 38: Multiplexer
From truth table functional description can be represented in a functional table.
The output can be expressed as follows
E |  |  | 
0 | X | X | 0
1 | 0 | 0 | 
1 | 0 | 1 | 
1 | 1 | 0 | 
1 | 1 | 1 | 
E |  |  | 
0 | X | X | 0
1 | 0 | 0 | 
1 | 0 | 1 | 
1 | 1 | 0 | 
1 | 1 | 1 | 

## Slide 39: Multiplexer
Several multiplexer are available in IC packages.
The 4 to one multiplexer can be implemented as shown in figure

## Slide 40: Multiplexer
Logic Design using Multiplexers
MUX is ideal to implement functions expressed as a sum of their minterms.
Let us look on 8 to 1 MUX
0 | 0 | 0 | 
0 | 0 | 1 | 
0 | 1 | 0 | 
0 | 1 | 1 | 
1 | 0 | 0 | 
1 | 0 | 1 | 
1 | 1 | 0 | 
1 | 1 | 1 | 
0 | 0 | 0 | 
0 | 0 | 1 | 
0 | 1 | 0 | 
0 | 1 | 1 | 
1 | 0 | 0 | 
1 | 0 | 1 | 
1 | 1 | 0 | 
1 | 1 | 1 | 

## Slide 41: Multiplexer
Logic Design using Multiplexers
Let enable E=1. equation for a 8 to 1 MUX with reference to figure can be written as

## Slide 42: Multiplexer
Logic Design using Multiplexers
To implement a three variable function expressed in terms of its minterms, simply needed to set the data input lines as for and for

## Slide 43: Multiplexer
Example 1: Implement the following function using 8 to 1 MUX.
Example 2: Implement following function using 4 to 1 MUX
Example 3: Implement using 4 to 1 MUX using b and c as the address lines.

## Slide 44: Demultiplexer
It is the reverse operation of the multiplexer.
A demultiplexer has an input line, output lines and n select lines.
A demultiplexer is the logic circuit that receives information through a single input line and transmits the same information over one of the possible output lines.
The output line that gets the information present on the input line is decided by the bit status of the selection lines.

## Slide 45: Demultiplexer
Example of 1 to 4 DEMUX
Input | Select |  | Output |  |  | 
 | a | b |  |  |  | 
1 | 0 | 0 | 1 | 0 | 0 | 0
1 | 0 | 1 | 0 | 1 | 0 | 0
1 | 1 | 0 | 0 | 0 | 1 | 0
1 | 1 | 1 | 0 | 0 | 0 | 1
Input | Select |  | Output |  |  | 
 | a | b |  |  |  | 
1 | 0 | 0 | 1 | 0 | 0 | 0
1 | 0 | 1 | 0 | 1 | 0 | 0
1 | 1 | 0 | 0 | 0 | 1 | 0
1 | 1 | 1 | 0 | 0 | 0 | 1

## Slide 46: Tutorials

## Slide 47: Tutorials
Implement a full adder circuit with a decoder and two OR gates.

## Slide 48: Homework
Study on
  Look ahead Carry adder

## Slide 49
49
Notes: 49

## Slide 50
Next Lecture
50
Notes: 50