## Slide 1: Uniform plane wave L3

## Slide 2: Polarization of Uniform Plane Waves
The polarization of uniform plane waves is defined as time varying behavior of the electric field intensity vector at some fixed point in space, along the direction of propagation
Types of polarization of a uniform plane wave
Linear polarization
Elliptical polarization
Circular polarization
In other words, the polarization is nothing but away in which the magnitude and direction of the electric field varies

## Slide 3
Linear Polarization
Consider that the electric field has only x-component and y-component of is zero
Then looking from the direction of propagation, the wave is said to be linearly polarized in x-direction
Similarly if only the y-component in is present and x-component of is zero then the wave is said to be linearly polarized in y-direction
Let us assume that both the components of are present denoted by and
The electric field is the resultant of andand the direction of it depends on the relative magnitude of and

## Slide 4
Linear Polarization
The angle made by with x-axis is given by,
The resultant vector is oriented in a direction which is constant with time, thus the wave is said to be linearly polarized
Thus when and components are in phase with either equal or unequal amplitudes, for a uniform plane wave travelling in z-direction, the polarization is linear

## Slide 5
Elliptical Polarization
Consider that the electric field has both the components which are not having same amplitudes and are not in phase
As the wave propagates, and will have maximum and minimum amplitudes at different instants of time depending on the relative amplitudes of and at any instant of time
In other words, the direction of the resultant field varies with time
If the locus of the end points of is traced, it is observed that moves elliptically

## Slide 6
Elliptical Polarization
Then such a wave is said to be elliptically polarized as shown in the figure below

## Slide 7
Elliptical Polarization
With 90-phase difference between and ;
The major axis of an ellipse lies along y-axis if the amplitude of is greater than that of the component and
The major axis of an ellipse lies along x-axis, if the amplitude of is greater than that of
Thus when the components and of unequal amplitudes have a constant, non-zero phase difference between two, for a uniform plane wave travelling in z-direction, the polarization is elliptical

## Slide 8
Circular Polarization
Let us consider that has two components, and , of equal amplitude but the phase difference between them is exactly 90
At any instant of time, when the amplitude of any one of the component is maximum, then the amplitude of the remaining component becomes zero
If is projected on a plane perpendicular to the direction of propagation, then the locus of all such points is a circle with the Centre on z-axis
If is having components in both x and y-directions, we can write,

## Slide 9
Circular Polarization
If is having components in both x and y-directions, we can write
Any electric wave has two components ;
Forward travelling component sin ()
Backward travelling component sin ()
Thus when two components and of equal amplitudes have a constant, non-zero phase difference of 90-between them, for a uniform plane wave, the polarization is circular

## Slide 10: Conditions for the Polarization of a Sinusoidal Wave
Time varying is given by,
Let be the phase difference between the two components ( and )
The two components can be expressed in phasor form as,

## Slide 11: Conditions for the Polarization of a Sinusoidal Wave
As the electric field vector is the resultant of and , we can write,

## Slide 12
From equations above, we can write,

## Slide 13
Also,

## Slide 14
Squaring both the sides,
Simplifying above equation,
Above equation is the equation for polarization of sinusoidal wave
By applying different conditions to equation for the polarization of sinusoidal wave, we get different types of the polarization

## Slide 15
Condition 1: and components are in phase i.e. =0.
The wave is said to be linearly polarized wave

## Slide 16
Condition2 : and components of unequal amplitudes with a phase difference 0.
Let us assume that =
Then equation becomes
The equation is said to be elliptically polarized

## Slide 17
Condition3: and components of equal amplitude with the phase difference between two as =
Let the amplitude of and be equal to
Thus the wave, with the components specified in the condition is said to be circularly polarized