## Slide 1: INTRODUCTION TO 3D MODELING AND IMAGE ACQUISITION

## Slide 2: 3D Scanning
3D Scanning Is a fast and accurate method of creating 3d scan data, which consists of putting physical measurements onto a computer in an organized manner
All of the physical dimensions from the object can be taken once the scan data is on the computer.
The information can then be converted to a computer-aided design (CAD) model or a computer-aided engineering (CAE) tool.

## Slide 3
METHODS OF COLLECTION
LASER SCANNING
Laser scanning
(or “lidar,” which stands for Light Detection And Ranging, a specific type of laser scanning,
but which is now often used as a catch-all term for laser scanning in general)
Is a broad term that encompasses a number of technologies that use lasers to determine the
locations of 3D points.
At its most basic, laser scanning emits laser pulses and then collects information about what
happens to those laser pulses.
That information is indexed into a computer file called a point cloud.
The more lasers that are emitted and collected, the denser your point cloud will be

## Slide 4
Types of Laser Scanning
1. Time of Flight (also known as “pulse based”)
As the name suggests, time-of-light laser scanners emit laser pulses and then determine object location by measuring the amount of time it takes for that laser pulse to bounce off an object and return to the scanner.
Each manufacturer may have their own different “flavor” of time-of-flight scanning, in terms of how they receive the laser pulses and analyze the return.
Pros: These scanners can measure things a great distance away.
Cons: They’re relatively “slow.” They can collect about 50,000 points a second.

## Slide 5
2.Time of Flight (airborne)
Airborne collection of 3D data can often use something called waveform processing and echo digitization, which is a form of time-of-flight scanning.
This type of ToF can get multiple returns from the same pulse of laser light, which allows you to get multiple readings from the same laser.
This is particularly useful if there are objects in the way of what you’re trying to scan, such as trees blocking the surface of the Earth.
In this way, it is possible to use software to remove all the returns that are clearly trees and vegetation and get smooth-earth point clouds, which are used for things like digital terrain models that are helpful in creating things like flood maps.

## Slide 6
3.Phase-based
These scanners emit a continuous laser beam and the scanner can tell by the modulations of the phase of the laser the location of whatever the laser runs into.
Because the laser is essentially continuously gathering data, it can very quickly gather many points and therefore provide a great deal of data.
Pros: These scanners are very fast, gathering as much as one million points per second.
Cons: These scanners can only gather data out to about 80 meters at the most. Also, the amount of data they collect can create file sizes that are difficult to manage.

## Slide 7
Handheld/Close-range
A number of manufacturers make “close-range” or “hand-held” laser scanners, which are primarily used to capture objects about the size of a person, or smaller.
However, these are increasing in utility and it is not uncommon now for someone to use a handheld laser scanner to scan something the size of a car or small airplane.
Some of these laser scanners require targets (essentially stickers) to be placed on the object ahead of time.
Others do not require targets and use software to essentially match features to each other. Some of these close-range scanners can attain very high accuracy, well below 1mm

## Slide 8
PHOTOGRAMMETRY
Photogrammetry (also sometimes known as stereoscopy) is a science dating to the 1850s that determines distances using photographs to take measurements.
In the last few years, great gains have been made in the algorithms that allow for measurements to be taken much faster, leading to software that can now create very large point clouds by ingesting thousands, even tens of thousands, of photographs.
Types of Photogrammetry
a.Take one measurement at a time,
With targets One type of photogrammetry software allows you to put out targets in a scene, take a number of overlapping photographs from a number of angles, ingest those photos, then manually identify which targets are the same in which photographs.
After doing those manual operations, the software is then able to tell you the distance between two points in 3D space. T
his type of software can be useful for creating diagrams of scenes, and is commonly used in the forensic marketplace and in the plant and process industry.

## Slide 9
b.Ingest all the photos,
Create a point cloud Some software packages are now able to automatically identify similar features from one photograph to another, and no longer need targets in the scene at all.
With this software, you simple ingest as many photographs as you have, and the software spits back out either a point cloud or a mesh model.
This software is becoming relatively ubiquitous, and is even offered as a free app for smartphones.
However, the quality of the models and point clouds produced varies widely

## Slide 10
STRUCTURED LIGHT SCANNERS
Structured light scanners project a single line of light, or a pattern of light, onto an object, and then use a camera (or more than one) and software to measure how that light is distorted, which can then be used to create a point cloud or model.
Types of Structured Light Scanners
a. Static
The light source and the cameras are in fixed locations, while the object to be scanned is placed in the field of vision of the cameras and the light source.
Sometimes the cameras and light sources are arrayed in a full 360-degree structure, allowing the entire object to be captured in 3D at once.
b. Handheld
Like handheld laser scanners, handheld structured light scanners can be swept over an object - sometimes with targets attached, sometimes without – creating a point cloud or model as more of the object is covered with the light source

## Slide 11
SONAR
While sonar, the process of using sound waves to establish position, has traditionally been a 2D technology, new advancements in technology have allowed manufacturers to create 3D sonar systems that are also capable of producing point clouds of underwater environments.
Types of Sonar
a.Single Beam
This is the “traditional” type of sonar, which can establish 3D position in a narrow path with a “ping” of sound.
With enough measurements, maps can be created of underwater areas. It is equivalent to an underwater total station of sorts in that you’re gathering one point of data at a time.
b. Multi-Beam
A multi-beam sonar system can gather a point cloud of wide swaths of the bottom of a body of water, or, when tightly focused, can create very dense point clouds of underwater objects.
This technology can be used to map and model things like offshore drilling platforms, shipwrecks,

## Slide 12
c. Robust Multi-Beam
It is possible by using a large number of sonar “beams” at a high rate of pings-per-second to create real-time 3D images of underwater objects.
This is different from multi-beam sonar in that the images do not have to be post-processed in order for the 3D nature of the data to be realized.
The 3D imagery can be consumed like video, looking at underwater objects as they are moved around, for example, and not having to take a picture and then look at what you captured back in the office.

## Slide 13: 3D DATA CAPTURE
3D Data Capture Is the process of gathering information from the real world, with x, y, and z coordinates, and making it digital
From there, it can be processed in a number of ways to create any number of end products: point clouds, 3D models, line drawings, fly through visualizations really, the possibilities are endless.
Types Of 3D Data
1.Georeferenced -every location in the world can be described as an x, y, z point. it has a latitude (x), a longitude (y),and an elevation (z).
Using a combination of GPS satellite technology and traditional survey techniques, any point can be established relatively quickly

## Slide 14
If you start collecting data from a “known point” you can then know with relative certainty what the georeferenced position is of every point that you gather.
If your data is properly georeferenced, it can be combined with data collected anywhere in the world and it will be properly referenced together
You could take measurements and have them be accurate to whatever degree your collection technology is accurate.
2. Non-georeferenced
If you do not start from a known point, you can still collect 3D data, but the data you collect will only be referenced to itself.
You can take measurements within the data, and they will be as accurate as your collection technology allows, but they will be only part of what in the industry is called a “pretty picture

## Slide 15
There can be many uses for this kind of data – from reverse engineering to crime scene documentation – but it will have limited value if you are trying to combine that data with data collected at other times or in other locations.